## Slide 1
Shape Adaptive Grinding (SAG)
Notes: 1.7.2013
1
‹#›

## Slide 2
MOTIVATION
Why SAG? — The Problem with Conventional Grinding
Core Idea: Conventional grinding is too aggressive for advanced materials and complex shapes.
High Contact Forces
Large rigid wheel creates concentrated force → stress concentrations on workpiece surface.
Surface & Subsurface Damage
Brittle materials (ceramics, coatings) fracture instead of deforming → cracks, chipping, residual stress.
Freeform Surfaces Unsupported
Rigid tools cannot conform to curved or complex geometries → uneven material removal.
Nano-finish Unachievable
Achieving Ra < 50 nm with rigid abrasives requires extreme process control — often impossible on hard materials.
Notes: 1.7.2013
2
‹#›

## Slide 3
CONCEPT
What is Shape Adaptive Grinding?
Core Idea: "SAG combines grinding precision with polishing flexibility — the tool adapts to the workpiece, not the other way around."
Definition
    A compliant (flexible) abrasive finishing process
    The grinding tool deforms under load to match the workpiece surface geometry
    Creates area contact instead of line or point contact
    Forces are distributed across many abrasive grains simultaneously
    Bridges the gap between grinding (material removal) and polishing (surface quality)
Key Distinction
Conventional Grinding:Rigid wheel → fixed geometry → line contact → high local force
Shape Adaptive Grinding:Flexible tool → conforms to surface → area contact → distributed low force
Result: Gentle, uniform material removal across the entire contact zone
Notes: 1.7.2013
3
‹#›

## Slide 4
TOOL DESIGN
Tool Structure & Contact Mechanics
Layered Tool Architecture
① Base Wheel (Rigid)
Provides rotational drive and structural support. Transmits torque from spindle.
② Elastic Layer (Polyurethane)
The key to adaptability. Compresses under load, allowing the tool to conform to workpiece curvature.
③ Abrasive Layer (Diamond Pad)
Fine diamond abrasives bonded to flexible backing. Directly contacts and removes material.
How Contact Evolves Under Load
Initial Touch — Line Contact
Tool first touches workpiece at a single line. All force concentrated at one edge.
Elastic Compression
Polyurethane layer deforms inward. Contact zone begins to spread outward.
Elliptical Area Contact
Pressure is now distributed over an elliptical patch. Highest at center, tapering at edges — like Hertzian contact, but compliant.
Notes: 1.7.2013
4
‹#›

## Slide 5
MECHANISM
Material Removal: Micro-Cutting & Ductile vs. Brittle Mode
How Each Abrasive Removes Material
01
Many Abrasives Act Together
Hundreds of diamond grains within the contact ellipse engage the surface simultaneously.
02
Each Grain — Tiny Penetration
Individual grain depth (h) is in the nanometer range. Each cuts a micro-groove in the surface.
03
Cumulative Material Removal
Total MRR = sum of all micro-cuttings. Low force per grain → no fracture → smooth finish.
Key Insight: "Low force per abrasive → ductile deformation → nano-level surface quality"
Ductile vs. Brittle Removal Mode
❌ High Force (Conventional)
    Force per grain exceeds material's fracture toughness
    Brittle fracture: cracks, chipping, pitting
    Poor surface integrity
    Subsurface damage propagates
✅ Low Force (SAG)
    Force per grain stays below critical threshold
    Ductile deformation: plastic flow, micro-grooving
    Smooth, crack-free surface
    Even ceramics behave ductile at nanoscale!
SAG enables ductile-mode machining even on inherently brittle materials — this is its most powerful advantage.
Notes: 1.7.2013
5
‹#›

## Slide 6
PROCESS PARAMETERS
Process Parameters & Their Effects
Three primary parameters govern SAG performance — understanding their interplay is essential for process design.
Wheel Speed (N)
↑ Speed → ↑ Abrasive interactions per second
    More grain passes over surface per unit time
    ↑ MRR at same contact force
    Generates more heat — balance carefully
Wheel Compression (T)
↑ Compression → ↑ Contact area → ↑ Force & MRR
    Controls how much elastic layer deforms
    Larger contact patch = more active grains
    Too much compression → risk of brittle damage
Abrasive Size (dg)
↓ Grain size → ↓ Penetration depth → ↑ Surface quality
    Smaller grains = shallower cuts
    Finer finish but lower MRR
    Chosen based on final Ra target
Notes: 1.7.2013
6
‹#›

## Slide 7
PERFORMANCE
Key Results & SAG vs. Conventional Grinding
Demonstrated Performance Outcomes
~20nm
Surface Roughness (Ra)
Nano-level finish achievable on ceramics and hard coatings — impossible with rigid grinding.
less
Subsurface Cracks
Ductile-mode removal eliminates crack propagation below the surface.
↓↓
Residual Stress
Distributed low forces drastically reduce thermomechanical stress in the workpiece.
Head-to-Head Comparison
Parameter
Conventional
SAG
Contact Type
Line / Point
Elliptical Area
Force Level
High (concentrated)
Low (distributed)
Surface Finish
Micron-scale Ra
Nano-scale Ra (~20 nm)
Removal Mode
Brittle fracture
Ductile deformation
Complex Shapes
Poor conformity
Excellent conformity
Subsurface Damage
Common
Eliminated
Notes: 1.7.2013
7
‹#›

## Slide 8
APPLICATIONS
Where SAG Makes the Difference
SAG is purpose-built for materials and geometries where conventional grinding fails.
Aerospace Thermal Barrier Coatings
Finishing WC-Co and ceramic coatings on turbine blades without delamination or cracking.
Optical & Precision Components
Achieving sub-20 nm Ra on glass, ceramics, and optical crystals for lens and mirror applications.
Additive Manufacturing Post-Processing
Finishing rough AM surfaces (metal/ceramic) that have complex, freeform geometries.
Freeform Surfaces & Molds
Conforming to sculptured surfaces in mold & die making where rigid tools leave unground zones.
Notes: 1.7.2013
8
‹#›

## Slide 9
SUMMARY
Key Takeaways
SAG represents a fundamental shift in thinking about abrasive finishing — compliance is a feature, not a limitation.
1
Compliant Tool = Adaptive Contact
The elastic layer enables the tool to conform to workpiece geometry, creating distributed elliptical area contact — the foundation of all SAG advantages.
2
Low Force per Grain → Ductile Mode
By keeping individual grain forces below the fracture threshold, SAG achieves ductile-mode material removal even on ceramics and hard coatings.
3
Nano-Scale Surface Quality
Surface roughness Ra ~20 nm with zero subsurface damage and minimal residual stress — far beyond what rigid grinding can achieve.
4
Ideal for Advanced Materials & Complex Geometries
Aerospace coatings, optical components, additive manufacturing, turbine blades — SAG fills the critical gap left by conventional processes.
The Big Picture: SAG is not just a better grinder — it is a different philosophy of finishing: gentle, distributed, adaptive, and geometry-aware.
Notes: 1.7.2013
9
‹#›